## Slide 1: Pitch Shift
Real-time Speech FPGA Implementation
Jake Garrison & Jisoo Jung

## Slide 2: Our Project Goal
Realtime pitch shifting optimized for speech
Optional Features
Input melody based pitch shift (autotune)
Harmony capabilities to output multiple pitch shifts to simulate a chorus
Autotune
Chorus

## Slide 3: History
Definition: Pitch shifting is a sound recording technique in which the original pitch of a sound is raised or lowered
Before digital sound, this it was extremely difficult to shift the pitch by non interval values
With tape or vinyl you could change pitch by altering the speed of playback
  Example: Alvin and the chipmunks
Analog octave pitch shift can be done with rectifier circuit
  Example: Jimi Hendrix or Led Zeppelin guitar hardware

## Slide 4: Applications
Voice Privacy
Voice Gender or Age Change
Other Voice Effect
  Darth Vader, Alvin and the Chipmonks, SciFi Robot voice
Text to speech / Speech synthesis
Auto Tune / Pitch Correction
Harmony / Chorus
Karaoke
Sampling / Resampling Audio

## Slide 5: Motivation
Seemed challenging… and is
Fun to play with
Popular in modern music
  Most pop music relies on pitch correction
Voice privacy is becoming important
Commercial software implementations are expensive
Hardware implementations is even more expensive
Software
Hardware

## Slide 6: Existing Methods
Analog
  Rectifier Circuit (octave only)
Time Domain
  PSOLA
  Delay Based
Frequency Domain
  Phase Vocoder
Physical Modeling
  Speech processing, inverse filtering (complex)

## Slide 7: Time Domain Pitch Shift
PSOLA (Pitch Synchronous Overlap/Add)
‘P’ will resample the sound, changing the pitch
  Uses decimation, then LPF, then interpolation to achieve non-integer resampling
  This changes the duration
‘S’ uses correlation so synchronize the ‘OLA’
  Uses correlation to find the best way to overlap and add the stretched or compressed sections
‘OLA’ is overlap and add
  This is what will stretch or compress the sample to the original length
Pros:
Fast to process
Simple
Ideal for tones
Cons:
Reverberation
Lower Quality

## Slide 8: Resampling
Resampling changes pitch
Stretching maintains original sample length
Both are needed!
Integer resampleing is easy
  2x upsample, insert 0s every other sample
  2x downsample, remove every other sample
Pitch shift requires non-integer resampling (stretch by 1.5, resample by 1/1.5)
    Decimation: downsamples and filter
    Interpolation: filter then upsample
    FIR filter used to obey Nyquist (no aliasing!)

## Slide 9: Time Domain Pitch Shift (continued)
Delay Based (Doppler Effect)
Remember the Doppler effect (sirens)
Conceptual: Imaging capturing a moment when the siren pitch is shifted, and repeating it…perpetually
This nifty algorithm does this, and doesn’t require resampling or FFT or filters!
Can actually be done with tape (Wendy Carolos)
Relies on two independent delays crossfading
Best for our FPGA friend
Pros:
Fast to process
No filtering
No resampling
Better than SOLA
Cons:
Unwanted random frequencies
Confusing

## Slide 10: Frequency Domain Pitch Shift
Phase Vocoder
Relies on STFT manipulation
Steps
  Analysis (Both Domains)
    Windowing (hanning window), then FFT
    Overlap windows by X %
  Processing (Frequency Domain)
    Stretch spectral content (lots of math here!)
    Adjust phase to change pitch and transition between bins
  Synthesis (Time Domain)
    IDFT, then windowing to smooth
    Sample is time stretched
    Resample to pitch shift
Pros:
Best quality
Customizable
Ideal for speech
Cons:
Several FFT + arctan
Slow
Complex

## Slide 11: STFT
Piano above. Can see harmonics and decay. Shows, time, frequency and magnitude
Combine several FFTs to create STFT

## Slide 12: Current State
Matlab Demo
  Phase Vocoder (wav file)
  Delay Based (wav file)
  Post processing analysis
C Demo (compiles on Atom Processor)
  Phase Vocoder (wav file)
  Phase Vocoder (real-time)
  PSOLA (wav file)
  Delay Based (wav file)
Real-time FPGA
  Phase Vocoder
  PSOLA
  Delay Based
FAIL
SUCCESS
IN PROGRESS

## Slide 13: Original Timeline….LOL if only

## Slide 14: Timeline
Research, decide to go with phase vocoder
Matlab phase vocoder demo
Write proposal
Phase vocoder C implementation (first wav file, then realtime on Atom)
Phase VocoderFPGA attempt….lots of fail…algorithm takes too long to process
SOLA research…seems like it will be faster (last weekend)
SOLA C implementation (wav file)…resampling non integer is too complicated
Delay method research…faster and less complex
Delay Matlab Demo
Delay C implementation (yesterday)
Ping Pong buffer Research
Delay FPGA attempt (work in progress)
Make slides and present

## Slide 15: Struggles
Algorithms are complicated
  Lots of math
  Complex and hard to debug
  Not really covered in class or labs
Not many C implementation examples on the internet
No way to know if it works until you write the whole algorithm
  We don’t have much info on the hardware limitations
Try…Hope…Fail…Try…Hope…Fail…Try…Hope…Fail… 
Real-time processing
  Samples fill buffer before processing completes
  Solutions
    use faster algorithm… ugh
    find better hardware… no thanks
    write lower level code… no thanks
  Scheduling (Ping Pong buffer)

## Slide 16: Matlab Demo (440 hz sine Input)
Delay Method
Phase Vocoder

## Slide 17: Matlab Demo (Singing)
Delay Method
Phase Vocoder
Original
+12
-12
Original
+12
-12
* Note the shifted output is the same length

## Slide 18: C Demos
 | Original | Phase Vocoder |  | Delay Based * | 
Sample | 0 semitones Factor: 0 | +4 semitones Factor: 1.26 | -4 semitones Factor: 0.79 | +4 semitones Factor: 1.26 | -4 semitones Factor: 0.79
Sine Wave 440 Hz |  |  |  |  | 
Singing Voice |  |  |  |  | 
*Delay based semitone calculation is not correct

## Slide 19: Code Comparison
Phase Vocoder
  Matlab : ~180 lines
  C : ~450 lines
Delay Method
  Matlab : ~150 lines
  C : ~ 300
Delay C Code Snippet

## Slide 20: Real-time FPGA Processing
Fill input buffer
Process pitch shift for buffer
Play output while reading in new input
Heavy processing occurs in main, I/O sampling occurs in hardware interrupt
Note: this hinges on the fact that processing is faster than filling the buffer. This is not guaranteed… Ping Pong buffering helps

## Slide 21: Ping Pong Buffering

## Slide 22: PING PONG BUFFERING – play_and_fill

## Slide 23: Questions ?